Supplement Information

Calculation of simulated low-resolution reflectance measurement from higher-resolution data.

For example, intensity I0 at 6680 was defined as 100 after passing through the filter.

I0 at other wavelengths (6746-6616 nm) can then be calculated by I0 = f*100, where f is the ratio from filter transmission profile.

I0t total for the filter was simply the integrated intensities using

Subsequently, I1 (the intensity after reflected by the sample) at each wavelength was calculated as I1 = I0*T, where T is the transmittance from the high-resolution FT-IR spectrum. I1t total for the filter was calculated in a similar manner using

Finally, simulated reflectance, R, for the filter were calculated from R = I1t/I0t

Using an upland cotton sample and the 6680 ± 66 (6746-6614 nm) filter sample calculation, the intensity of the incident light at 6680 nm was defined as 100 units and that of light outside of the filter transmission range (6614-6746 nm) was set to zeros. Within this range, the incident intensity was calculated in 4.4 nm increments (same resolution as for the FT-IR spectrometer). From 6614 nm to 6680 nm, the equation becomes

Where  is the wavelength. Hence, from 6680 nm to 6746 nm, the equation

was then used. The resulting intensity for each wavelength is shown in Supplementary Table 1.

The total I0 for this filter is then:

The individual reflectance for this wavelength range with an upland cotton sample from FT-IR spectrum is listed in Supplementary Table 2.

I1 (The simulated intensity of the reflected radiation) at each wavelength was then calculated using I1 = I0*R

The resulting values of I1 are shown in Supplementary Table 3.

The calculated total reflected radiation for the filter was calculated using

And the simulated reflectance (R) for the 6680 nm filter was then, R = I1t/I0t = 90.14%.

Similar calculations were undertaken for each filter. The resulting simulated reflectance spectrum for each material was then generated. Representatives of those are shown in Supplementary Figure 1, Supplementary Figure 2 and Supplementary Table 4.